PACSAT Errors and Telemetry
Authors: Chris Thompson G0KLA / VE2TCP
Version: 1.00 – 21 Jun 2023
RED FS
Errors.h
ErrorType_t – enum that lists the error codes
struct localErrors – structure that stores the number of errors of each type. Global variable declared in main. (Currently this is defined as rt1_Errors_t in rt1Downlink.h
Errors.c
char *ErrMsg[] – list of error names for debug
char * TaskNames[] – list of task name strings for debugging that should (will) match ids in WdReporters_t in watchdogSupport.h
ReportError(ErrorType_t err,
bool f, ErrorInfoType_t t, int info) – Report an error of type err, setting the FATAL flag and reporting ErrorInfoType_t with some data stored in or pointed to by the info integer.
WOD and Experiment Files Broadcast by PB when requested by ground stations
Timing based on mode. e.g. SAFE mode, DATA mode
?
2
ReportError (
TXPacketDropped,
FALSE,
TaskNumber,
PbTaskWD)
2
Destination: encodes Frame Type
Format: AX25 UI frame – follows format for PB with PID 0xF0
Raw bytes: packed according to structure
(big or little endian?)
Key
Data
RTOS Event
2
RTOS Priority
RTOS Timer
struct:
localErrorsPayload
saveAcrossResets
I2C1ErrorCount
...
droppedPackets
XYZ Task
e.g. Task fails to add packet to TX Queue
struct:
wodHealthPayload
temperatures
currents
voltages
Telem & Control Task
Periodic task collects sensor and experiment telemetry or data
Struct:
expPayload
data0
data1
data2
BroadcastTelem Task
Periodic task creates broadcasts telemetry packets
struct:
healthFramePacket
Packet Header(s)
healthPayload
localErrorsPayload
TX PKT Queue
-----
-- ---- ---
---- ---
struct:
maxPayload
temperatures
currents/voltages
struct:
healthPayload
temperatures
currents/voltages
struct:
minPayload
temperatures
currents/voltages